## Slide 1: Address Resolution Protocol Forensics
Traffic files: ARP_spoofing
Notes: https://www.youtube.com/watch?v=6G3qm60dfA8&ab_channel=PrashantThombre

## Slide 2: Overview
ARP introduction
  APR protocol
  ARP tables
ARP table demo
Capture ARP traffic demo
ARP poisoning
  Capture ARP poisoning evidence
  Analysis evidence

## Slide 3: Address Resolution Protocol (ARP)
Motivation: When a device on a network wants to send data to another device, it needs to know the Media Access Control (MAC) address of the recipient. However, devices only know the IP address of other devices.
Approach: ARP protocol is used to map a network address (such as an IP address) to a physical address (such as a MAC address) on a local network.

## Slide 4
Ping uses both protocols

## Slide 5: How ARP Works
Device A (with IP1, MAC 1) wants to send data to Device B (with IP3, MAC 3) on the same network.
Device A sends an ARP broadcast request message to discover the physical address of Device B.
Device B responds with its physical address, and Device A can use this information to send the data to Device B

## Slide 6: What is ARP table (ARP cache)
A table used by a computer or network device to store mappings between IP addresses and MAC addresses on a local network.
  One table for each device
ARP table allows devices to communicate with each other efficiently on a local network
  without the need for manual configuration of MAC addresses.
ARP tables are also dynamic
  they can change over time as devices join or leave the network.
Neighbor IP | Neighbor MAC | Expire
192.168.1.1 | 00:1A:4F:62:7E:8D | 2m20s
192.168.1.25 | 08:21:58:BE:A4:F2 | 3m23s
A sample ARP table of a device in LAN

## Slide 7: Importance of ARP Protocol/ARP table
ARP is a critical protocol for the proper functioning of local area networks (LANs).
Without ARP, devices on a network would not be able to communicate with each other properly.
Understanding ARP is important for network administrators and anyone who works with computer networks.

## Slide 8: ARP tables demo
Create a working directory
Notes: sudo apt install python3-scapy
sudo apt install python3-pywin32

## Slide 9
type of hardware address
address was dynamically learned and is considered complete.
Remember the Mac address (:fc), we use it later

## Slide 10: Every device has an ARP table
Show ARP table of another device in LAN

## Slide 11: Manipulate ARP table entry
Assume we have another running machine in our network (LAN)
ping uses ARP protocol to find the target’s machine mac address
the new entry will be added to the ARP table
Add an entry to an ARP table using Ping

## Slide 12
Gateway IP | Gateway Mac
Victim IP | Victim Mac
Kali
Gateway IP | Gateway Mac
Victim IP | Victim Mac
Sample ARP tables

## Slide 13
Delete an ARP entry in Kali ARP table
Notes: https://www.thepythoncode.com/article/building-arp-spoofer-using-scapy
https://www.thepythoncode.com/article/make-dns-spoof-python
https://www.geeksforgeeks.org/python-how-to-create-an-arp-spoofer-using-scapy/

## Slide 14: Capture ARP traffic

## Slide 15
Check network interface using tshark
We will use eth0

## Slide 17
ARP request message
wget https:/raw.githubusercontent.com/frankwxu/digital-forensics-lab/main/Networking_Forensics/lab_files/ARP_spoofing/arp.pcap
wireshark arp.pcap

## Slide 18
ARP reply message

## Slide 19
ARP fields in Python scapy library vs. in Wireshark
Notes: sudo python3 -c "import scapy.all as scapy; print(scapy.ls(scapy.ARP))"

## Slide 20: ARP poisoning

## Slide 21: What is ARP Spoofing/Poisoning
A type of cyber attack where an attacker sends false Address Resolution Protocol (ARP) messages over a local area network (LAN).
  By doing this, the attacker can associate their own MAC address with the IP address of another device on the network, allowing them to intercept or modify data that is intended for that device.
ARP Spoofing attacks can be used to conduct man-in-the-middle (MITM) attacks, steal sensitive information, or cause network disruption.
Prevent ARP Spoofing
  network administrators can implement measures such as using ARP spoofing detection software, limiting the number of devices on the network, or using virtual LANs (VLANs).
Spoofing vs poisoning
  spoofing = using other’s identity/IP
  Poisoning = consequence of spoofing
Notes: https://www.thepythoncode.com/article/building-arp-spoofer-using-scapy

## Slide 22
Victim IP | Victim Mac
Gateway IP | Gateway Mac
Gateway IP | Gateway Mac
Before Attacking/ARP tables are clean

## Slide 23
Sending ARP response to the gateway (target) saying that "I have the victim's IP address, use my MAC to talk".
Sending ARP response to the victim (target) saying that "I have the gateway's IP address, used my MAC to talk".
Security Problem: Anyone (Attacker) can send an ARP response message to anyone (Victim/Gateway) on the LAN without an ARP request to poison anyone’s (Victim/Gateway’s) ARP table
Security consequence: The Victim/Gateway will go to whatever IP the attacker injected into their ARP tables.
Attacking/Poisoning ARP tables

## Slide 24
man-in-the-middle attack
act as a middleman
Victim IP | Attack’s Mac
Gateway IP | Attack’s Mac
poisoned ARP
After Attack/ARP tables were poisoned

## Slide 25: Download ARP poisoning attacking code
Download ARP attacking code from github
Get MAC address of a given IP
Notes: https://raw.githubusercontent.com/frankwxu/digital-forensics-lab/main/Networking_Forensics/lab_files/ARP_spoofing/arp.py
sudo python3 -c "import arp; print(arp.get_mac('136.160.215.194'))"

## Slide 26
a Python function that uses the Scapy library to obtain the MAC address of a device on a local network given its IP address.
The function takes an IP address as its argument.
It creates an ARP (Address Resolution Protocol) request packet using Scapy's ARP function and sets the "pdst" field to the IP address provided as an argument.
It creates an Ethernet broadcast frame using Scapy's Ether function and sets the destination MAC address to "ff:ff:ff:ff:ff:ff". This frame is used to broadcast the ARP request packet to all devices on the network.
It combines the ARP request packet and the Ethernet broadcast frame into a single packet using Scapy's "/" operator.
It uses Scapy's srp function to send the combined packet to the network and receive a list of packets in response within a timeout period of 5 seconds. The "verbose" argument is set to False to suppress output.
The function returns the MAC address of the first device that responds to the ARP request. This is obtained from the "hwsrc" field of the second element of the first element in the list of responses.

## Slide 27
a Python function that performs an ARP spoofing attack on a target device on a local network.
The function takes two IP addresses as arguments - target_ip and host_ip.
  target_ip is the IP address of the device whose ARP table we want to spoof, while
  host_ip is the IP address of the device that the target device wants to communicate with.
It creates an ARP packet using Scapy's ARP function and sets the op field to 2 to indicate an ARP reply packet. The pdst field is set to target_ip, the IP address of the target device, and the hwdst field is set to the MAC address of the target device, obtained using the get_mac function. The psrc field is set to host_ip, the IP address of the device that the target wants to communicate with.
It sends the ARP packet using Scapy's send function, with the verbose argument set to False to suppress output.
If verbose is True, the function prints a message indicating that an ARP reply packet has been sent to the target device, along with the MAC address of the attacker's own interface.
The attacker’s/Kali’s MAC is automatically attached to the ARP response

## Slide 29
Launch ARP poisoning Attacking

## Slide 31: Capture and Analyze ARP Spoofing Traffic

## Slide 32: How to capture ARP spoofing traffic

## Slide 33: Download traffic (Option)
wget https:/raw.githubusercontent.com/frankwxu/digital-forensics-lab/main/Networking_Forensics/lab_files/ARP_spoofing/arp.pcap

## Slide 34
targeting Victim

## Slide 36: Conclusion
ARP spoofing attacker spoofs or falsifies the IP in ARP messages.
ARP spoofing is similar to identifying theft
  Both ARP spoofing and identity theft involve a perpetrator deceiving the victim in order to gain access to sensitive information.
  ARP messages to trick other devices on the network into sending traffic to the attacker's device instead of the legitimate device, allowing the attacker to intercept and steal sensitive information

## Slide 37: Assignment
Repeat all slides
Use Kali and another machine to
  capture ARP protocol
  capture ARP spoofing
  Show poisoned ARP table